## Slide 1
Markus Hug 15.02.2016

## Slide 2
MPS Group Organisation
MPS Group
MPS Watch
MPS Precimed
MPS Décolletage
MPS Microsystems
150 employees
Location: Bonfol
Watch bearings and gear wheels
150 employees
Location: Bienne
Microsystems, ball screws, linear bearings
80 employees
Location: Corgémont
Orthopedic instruments
20 employees
Location: Court
Precision decolletage parts

## Slide 3
Located in Biel/Bienne, Switzerland
14’400 m2 built in 2008
150 employees
ISO 9001 – ISO 14001 - ISO 13485
Research & Development
Industrialization
Parts manufacturing :
  - turning, grinding,
  - ball bearing manufacturing,
  - thermal and surface treatment.
Microsystems assembly (clean room)
Purchasing and logistic
Quality assurance and Quality control
MPS Microsystems

## Slide 4
MPS Microsystems products and applications
Standard Products (Microlinea) | Engineered solutions
Ball screws Linear bearings (L-Line) Linear bearings (DBL lines) | Active implants Medical robotics Automation Optics Science Defense

## Slide 5: Robot Manufacturing Process
Markus Hug 15.02.2016

## Slide 6: Overview
Turning & Milling
Surface & Heat Treatment
Grinding & Finishing
Manufacturing
Raw materials
Assembly & Test

## Slide 7: Raw materials
Martensitic & austenitic stainless steels
Copper alloys
Aluminum alloys
Plastics
Special materials
Etc.

## Slide 8: Turning
Swiss-type turning
Usual tolerances | Usual run-out & concentricity | Usual hardness
± 6 µ for Ø < 10 mm ± 10 µ for Ø ≥ 10 mm | Down to 10 µ depending on part complexity | According to raw material
Holder

## Slide 9: Heat treatment
Usual tolerances | Usual run-out & concentricity | Usual hardness (AISI 440C)
- | ↗ Study of deformation due to heat treatment | Min. 61 HRC
Heat treatment :
Annealing
Quenching
Cryogeny
Tempering

## Slide 10: Grinding
Usual tolerances on Ø | Usual run-out & concentricity | Usual hardness (AISI 440C)
+/- 3 µ | 5 µ | Min. 61 HRC
Outer Ø and thread grinding
between centers
Inner Ø grinding – centerless,
rolling on grinded OD

## Slide 11: Grinding

## Slide 12: Milling
5-axis milling
Usual tolerances | Usual geometrical tolerances | Usual hardness
Down to ± 5 µ depending on part complexity | Down to 10 µ depending on part complexity | According to raw material
R2-Support

## Slide 13: Milling

## Slide 14: Surface treatment
Cleaning & degreasing
Vibratory deburring
Cutting oil, burrs, chips, etc.

## Slide 15: Other processes
Inner thread grinding
Polishing
Honing
Continuous feed centerless grinding
Lapping
Manual deburring & visual inspection

## Slide 16: Assembly
General assembly environment
Cleanroom class 100’000
Special assembly environment
Cleanroom class 10’000
Flow cells
Air stream class 1’000

## Slide 17: Assembly
Project specific assembly
Processes
Process manuals with visual aids
Tooling's
in the field of precision mechanics

## Slide 18: Assembly
Project specific assembly
In process controls
Measurement devices (Metrology)
in the field of precision mechanics

## Slide 19: Final Tests
Werth 3D measurement device
Optical and tactile
Resolution 0.5µm
Repeatability ±2µm
Measurements samples for the Actuator
X/Y Position accuracy
Max angular tilt R1 – R2